## Slide 1
CHAPTER 4
The Eight Step Process©:
An Overview

## Slide 2: Learning Objectives Overview
Knowledge Objectives
Skills Objectives

## Slide 3: Introduction (1 of 2)
On-scene response operations must:
  Be based on a structured and standardized system of protocols and procedures
  Rely on standardized procedures to bring consistency to the tactical operation

## Slide 4: Introduction (2 of 2)
The Eight Step Process© is widely used throughout the country by governmental and private sector hazardous materials response teams for the tactical management of hazardous materials emergencies.

## Slide 5: Making the Transition (1 of 2)
Early critical factors include:
  Timely establishment of command and control
  Responder recognition of clues indicating hazardous materials
  Quickly gaining scene control and removing bystanders from problem

## Slide 6: Making the Transition (2 of 2)
Basic considerations during the alerting, notification, and initial response phase include the following:
  Location of the incident?
  Available clues that hazmats involved?
  Reports or physical clues of any unusual odors?
  Any injuries or casualties involved?
  Any initial responders down?
  Any suspicious activity in the area?

## Slide 7: The Eight Step Process© (1 of 2)
Outlines basic tactical functions
Flexible guideline
Recognizes that the majority of incidents involving hazardous materials are minor in nature
Expands as the scope and magnitude of the incident grows
Provides a consistent management structure

## Slide 8: The Eight Step Process© (2 of 2)
These eight functions typically follow an implementation timeline at the incident:
  Site management and control
  Identify the problem
  Hazard assessment and risk evaluation
  Select personal protective clothing and equipment

## Slide 9: Step 1: Site Management and Control (1 of 3)
Function: Site management and control involves managing and securing the physical layout of the incident.
  Goal: Establish the playing field so that all subsequent response operations can be implemented safety and effectively.

## Slide 10: Step 1: Site Management and Control (2 of 3)
Checklist:
  During the initial approach to the incident scene, avoid committing or positioning personnel in a hazardous position.
  Establish a staging area (Level I, II) for additional responding equipment and personnel.
  Establish a hot zone or inner perimeter as the “playing field.”

## Slide 11: Step 1: Site Management and Control (3 of 3)
Checklist:
  Do not attempt to enter the area without the appropriate level of respiratory and skin protection, based on the hazards present.
  If civilians are injured and personal contamination is suspected, isolate all personnel until emergency decon can be established.
  Initiate public protective actions (PPA).

## Slide 12: Step 2: Identify the Problem (1 of 2)
Checklist:
  Survey the incident.
  Use clues for determining the identity of the materials involved.
  Consider factors in assessing the type of container involved.
  Conduct offensive or defensive reconnaissance, as necessary, to gather intelligence (or intel) on the situation.

## Slide 13: Step 2: Identify the Problem (2 of 2)
Function: Identify the scope and nature of the problem.
Goal: Identify the scope and nature of the problem, including the type and nature of hazardous materials involved.

## Slide 14: Step 3: Hazard Assessment and Risk Evaluation (1 of 5)
Function: The primary objective of the risk evaluation process is to determine whether or not responders should intervene, and what strategic objectives and tactical options should be pursued to control the problem.

## Slide 15: Step 3: Hazard Assessment and Risk Evaluation (2 of 5)
Goal: Assess the hazards present, evaluate the level of risk, and establish an incident action plan (IAP) to make the problem go away.

## Slide 16: Step 3: Hazard Assessment and Risk Evaluation (3 of 5)
Checklist:
  Assess the hazards posed by the problem.
  Collect, prioritize, and manage hazard data and information from all sources, as appropriate.
  Utilize primary technical information centers available to public safety personnel.

## Slide 17: Step 3: Hazard Assessment and Risk Evaluation (4 of 5)
Checklist:
  Air monitoring and the general hazmat behavior model are critical in implementing a risk-based response.
  Based on the risk evaluation process, develop your IAP.

## Slide 18: Step 3: Hazard Assessment and Risk Evaluation (5 of 5)

## Slide 19: Step 4: Select Personal Protective Clothing (1 of 5)
Function: Based on the results of the hazard and risk assessment process, emergency response personnel will select the proper level of personal protective clothing and equipment.

## Slide 20: Step 4: Select Personal Protective Clothing (2 of 5)
Goal:
  Ensure all emergency response personnel have the appropriate level of personal protective clothing and equipment (skin and respiratory protection) for the expected tasks.

## Slide 21: Step 4: Select Personal Protective Clothing (3 of 5)
Checklist:
  The selection of personal protective clothing will depend on the hazards and properties of the materials involved and the response objectives to be implemented.
  Several factors must be considered in evaluating the use of specialized protective clothing.

## Slide 22: Step 4: Select Personal Protective Clothing (4 of 5)
Checklist:
  Chemical vapor protective clothing—This is specialized chemical protective clothing, which, when used in conjunction with air-supplied respiratory protection devices, offers a sealed, integral level of full-body protection from a hostile environment.
  Ensure all emergency response personnel are using the proper protective clothing and equipment equal to the hazards present.

## Slide 23: Step 4: Select Personal Protective Clothing (5 of 5)
Checklist:
  Do not place personnel in an unsafe emergency situation or location.
  Order additional personnel and other specialized equipment and technical expertise early in the incident.

## Slide 24: Step 5: Information Management and Resource Coordination (1 of 5)
Function: Refers to proper management, coordination, and dissemination of all pertinent data and information within the ICS in effect at the scene

## Slide 25: Step 5: Information Management and Resource Coordination (2 of 5)
Goal: Provide for the timely and effective management, coordination, and dissemination of all pertinent data, information, and resources among all of the players

## Slide 26: Step 5: Information Management and Resource Coordination (3 of 5)
Checklist:
  Confirm the ICP is in a safe area.
  Confirm a unified command organization is in place and all key response and support agencies are represented directly or through the liaison officer.
  Expand the ICS and create additional branches, divisions, or groups, as necessary.

## Slide 27: Step 5: Information Management and Resource Coordination (4 of 5)
Checklist:
  Ensure all appropriate internal and external notifications have been made.
  Ensure safety procedures are part of all tactical briefings.

## Slide 28: Step 5: Information Management and Resource Coordination (5 of 5)
Checklist:
  Make sure there is continuing progress toward solving the emergency in a timely manner.
  If activated, provide regular updates to the local/facility emergency operations center.

## Slide 29: Step 6: Implement Response Objectives (1 of 4)
Function: The phase where emergency responders implement the best available strategic goals and tactical objectives, which will produce the most favorable outcome

## Slide 30: Step 6: Implement Response Objectives (2 of 4)
Goal: Ensure the incident priorities (i.e., rescue, incident stabilization, environmental and property protection) are accomplished in a safe, timely, and effective manner.

## Slide 31: Step 6: Implement Response Objectives (3 of 4)
Checklist:
  Implement response objectives.
  Ensure any detection or monitoring equipment is operational and properly calibrated.

## Slide 32: Step 6: Implement Response Objectives (4 of 4)
Checklist:
  Ensure entry teams have been briefed prior to being allowed to enter the hot zone.
  Conduct regular monitoring of the hazard area to determine if conditions are changing.

## Slide 33: Step 7: Decon and Clean-Up Operations (1 of 4)
Function: Decontamination (decon) is the process of making personnel, equipment, and supplies safe by reducing or eliminating harmful substances (i.e., contaminants) that are present when entering and working in contaminated areas (i.e., hot zone or inner perimeter).

## Slide 34: Step 7: Decon and Clean-Up Operations (2 of 4)
Goal: Ensure the safety of both emergency responders and the public by reducing the level of contamination on scene and minimizing the potential for secondary contamination beyond the incident scene.

## Slide 35: Step 7: Decon and Clean-Up Operations (3 of 4)
Checklist:
  Ensure the technical decon operations are coordinated with tactical operations.
  Incidents involving large numbers of contaminated or potentially contaminated individuals will require the establishment of a mass decon operation following the basic principles of mass casualty decon.

## Slide 36: Step 7: Decon and Clean-Up Operations (4 of 4)
Checklist:
  Ensure proper decon of all personnel before they leave the scene.
  Establish a plan to clean up or dispose of contaminated supplies and equipment before cleaning up the site of a release.

## Slide 37: Step 8: Terminate the Incident (1 of 4)
Function: To terminate emergency response activities and begin the initiation of post-emergency response operations (PERO)

## Slide 38: Step 8: Terminate the Incident (2 of 4)
Goal: Ensure overall command is transferred to the proper agency when the emergency is terminated and all post-incident administrative activities are completed per local policies and procedures.

## Slide 39: Step 8: Terminate the Incident (3 of 4)
Checklist:
  Account for all personnel before securing emergency operations.
  Conduct incident debriefing session for on-scene response personnel.
  Ensure command is formally transferred from the lead response agency to the lead agency for all post-emergency response operations.

## Slide 40: Step 8: Terminate the Incident (4 of 4)
Checklist:
  Ensure public safety units are aware of any hazards remaining at the incident scene in the event emergency responders must return to the scene.
  Ensure the elements of the response are documented.
  Ensure all emergency equipment is decontaminated, reserviced, inspected, and placed back in service.

## Slide 41: Summary (1 of 4)
Emergency response operations at incidents involving hazardous materials must always be based on a structured and standardized system of response protocols and procedures.

## Slide 42: Summary (2 of 4)
The Eight Step Process© is a tool used for the tactical management of hazardous materials emergencies.
Although the level of equipment, training, and personnel may vary among organizations, there are fundamental functions and tasks that must be evaluated and implemented on a consistent basis.

## Slide 43: Summary (3 of 4)
The eight functions within the Eight Step Process© are:
  Site management and control
  Identify the problem
  Hazard assessment and risk evaluation
  Select personal protective clothing and equipment

## Slide 44: Summary (4 of 4)
The eight functions within the Eight Step Process© are:
  Information management and resource coordination
  Implement response objectives
  Decon and clean-up operations
  Terminate the incident